## Slide 1: Application of Non dominated Sorting Genetic and Particle Swarm Optimization Process for solving machine loading problem in Flexible Manufacturing Systems

## Slide 2: Introduction to FMS and Evolutionary algorithms
FMS stands for flexible manufacturing system. Flexibility is of two types machine flexibility and routing flexibility. FMS contain automated CNC machines , material handling and central control computer
Evolutionary algorithms are population based metaheuristic optimization algorithms. EA are inspired from nature.
EA are being used by various authors for scheduling the FMS job sequence

## Slide 3: Objectives
To determine the job sequence in Flexible manufacturing system using evolutionary algorithms
To validate and develop an algorithm which will reduce the system unbalance and increase throughput and reduce the penalty cost for excluding any job

## Slide 4: Problem Definition
Random FMS multiple machines and fixed tool slots
We have 8 different part types
Each part type have different number of operations.
Given data:
Here 4 machines are available.
Each machine has 8 hours of time and 5 tool slots available .
Part types are arriving randomly in a given planning period and their operation times and tool slot requirements are well known
The random FMS considered here is capable of performing operations that may be essential or optional. Essential operations are those that can be carried out on a particular machine using particular tool slots

## Slide 5
Part type | Operation no. | Batch size | Unit processing time | Machine no. | Tool slots needed | Penalty cost (If not selected)
1 | 1 | 8 | 18 | 3 | 1 | 20
2 | 1 | 9 | 25 | 1 | 1 | 13
 |  |  | 25 | 4 | 1 | 
 | 2 |  | 24 | 4 | 1 | 
 | 3 |  | 22 | 2 | 1 | 
3 | 1 | 13 | 26 | 4 | 2 | 15
 |  |  | 26 | 1 | 2 | 
 | 2 |  | 11 | 3 | 3 | 
4 | 1 | 6 | 14 | 3 | 1 | 25
 | 2 |  | 19 | 4 | 1 | 
5 | 1 | 9 | 22 | 2 | 2 | 29
 |  |  | 22 | 3 | 2 | 
 | 2 |  | 25 | 2 | 1 | 
6 | 1 | 10 | 16 | 4 | 1 | 22
 | 2 |  | 7 | 4 | 1 | 
 |  |  | 7 | 2 | 1 | 
 |  |  | 7 | 3 | 1 | 
 | 3 |  | 21 | 2 | 1 | 
 |  |  | 21 | 1 | 1 | 

## Slide 6
7 | 1 | 12 | 19 | 3 | 1 | 17
 |  |  | 19 | 2 | 1 | 
 |  |  | 19 | 4 | 1 | 
 | 2 |  | 2 | 1 | 1 | 
 |  |  | 13 | 3 | 1 | 
 |  |  | 13 | 1 | 1 | 
 | 3 |  | 23 | 4 | 1 | 
8 | 1 | 13 | 25 | 1 | 1 | 26
 |  |  | 25 | 2 | 1 | 
 |  |  | 25 | 3 | 1 | 
 | 2 |  | 7 | 2 | 1 | 
 |  |  | 1 | 1 | 1 | 
 | 3 |  | 24 | 1 | 3 | 
Problem adapted from Sankar and Srinivasulu(1989)

## Slide 7
Mathematical Model

## Slide 9
Variables Used

## Slide 10: Non dominance
Dominance
A decision vector “k” is said to dominate decision vector “p” if the following two constraints satisfies:
fi(k) ≥ fi(p) For all i belongs to ( i = 1,2,…….m)
fi(k) > fi(p) for at least one i which belongs to (1,2,……m)
Pareto optimal solutions in min-min-min function
as visualized in 3 dimensions

## Slide 11
Given two solutions
F(x) =
F(y) =
Normalized distance
0 Otherwise
Sharing function
where P is distance
and σshare is given by
L is number of objectives
N is number of population
Niche count
where dpk is the distance between pth point and
kth point and z(ri) is the number of members
in the front with same rank ri

## Slide 12: What are the extensions considered for the project?
Multi objective function is solved by assigning fitness determined by Non Dominated sorting procedure
A hybrid algorithm has been considered rather than single Genetic algorithm another algorithm Particle swarm has been added
Multiple objective has been considered with three objectives of which two are to be minimized and another is to be maximized, namely System unbalance, Penalty cost & Throughput .

## Slide 13
Non dominated sorting Genetic algorithm process:
Coding scheme: Pheno style coding scheme.
Feasible job sequence is coded as indicating the job sequence as two digit number
Example: Parent1: 01 05 08 02 06 09 03 07 10 04 --- for a 10 job sequence
Reproduction (Selection) scheme: Roulette selection
Crossover scheme : Single point or cycle crossover is considered
Example
Two point crossover
Mutation scheme:
With pheno type coding two random positions are selected and the positions are swapped
Fitness evaluation
Non dominated sorting fitness

## Slide 14
NSGA Flow chart
start
Evaluate fitness function
Input all required values
Iter=1
Non dominated sorting evaluation
pop=1
Is population<population size
Pop =pop+1
Yes
No
Compute new values
Is Iter<Iteration size or best possible value achieved
Yes
stop
No
roulette selection (update mating pool)
Crossover probability(pc)=0.9
Mutation
Probability(pm)=0.005

## Slide 15
Dimension j | 1 | 2 | 3 | 4 | 5 | 6
 | 0.11 | 1.48 | 1.21 | 0.45 | 1.08 | 0.32
 | 3.89 | 2.94 | 3.08 | -0.87 | -0.20 | 3.16
Job sequence | 1 | 6 | 4 | 5 | 3 | 2
Non dominated sorting Particle swarm optimization process:
Obtained by spv rule if initialized
is the best position of particle i and is the global best
is the velocity of the particle and is weight associated from the previous iteration
A sample representation of a job scheduling is given as below

## Slide 16
NSPSO Flow chart
start
Evaluate fitness function
Input all required values
Iter=1
Non dominated sorting evaluation
pop=1
Is population<population size
Pop =pop+1
Yes
No
Store pbest and gbest values
Update x,v,w using the equations
Compute new values
Is Iter<Iteration size or best possible value achieved
Yes
stop
No

## Slide 17: Solution Methodology Flow Diagram
Random function
Activate PSO
Initialize
PSO algorithm process
Activate GA
If value >= 0.5
If value < 0.5
Global best from GA
iterations< max iterations
Yes
No
Yes
No
GA algorithm process
Global best from PSO
Stop and return Global best
iterations< max iterations
Stop and return Global best
Iterations=iterations +1
Iterations=iterations +1
Convert global best to weight array
Convert global best to job sequence
Add it to the population of GA
Add it to the population of PSO

## Slide 18: Input format
The input is provided in a text file.
Two inputs are given to the problem one being the constraints for each operation and tool slots needed
Other being Resources available for the machine
First row indicates the machine time available for each machine
Second row indicated the tool slots available on each machine
Third row indicates the penalty cost for not considering a part type
Fourth row contains the batch sizes for each part type

## Slide 19: Results
Key Parameters | Notation | Value
NSGA |  | 
Population size | N | 20
Cross over probability | Pc | 0.8
Mutation probability | Pm | 0.05
Selection | - | Roulette selection
Maximum number of iterations | K | 100
NSPSO |  | 
C1,C2 | C1,C2 | 2,2 respectively
Inertial weight | Wt | 2
Decrement factor | β | 0.5
Non dominated Sorting |  | 
Alpha | α | 1
Sharing factor | σ | From table

## Slide 20
Chart: Non dominated sorting Genetic algorithm
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
System Unbalance | 411 | 18 | 18 | 10 | 6 | 10 | 18 | 25 | 6 | 18
Throughput | 35 | 46 | 46 | 37 | 43 | 37 | 46 | 34 | 43 | 46
Total penalty cost incurred | 111 | 93 | 72 | 93 | 93 | 74 | 72 | 72 | 74 | 72
Number of iterations

## Slide 21
Chart: Particle swarm optimization algorithm
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
System unbalance | 576 | 65 | 18 | 18 | 7 | 18 | 10 | 6 | 7 | 6
Throughput | 32 | 46 | 46 | 46 | 46 | 46 | 37 | 43 | 37 | 43
Penalty cost | 101 | 93 | 72 | 72 | 59 | 72 | 74 | 70 | 72 | 70
Number of iterations

## Slide 22
Chart: NSGA & Pso
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
System unbalance | 6 | 7 | 6 | 7 | 18 | 6 | 7 | 6 | 6 | 7
Throughput | 43 | 50 | 46 | 50 | 46 | 46 | 50 | 46 | 43 | 50
Penalty cost incurred | 93 | 59 | 59 | 59 | 72 | 72 | 59 | 70 | 70 | 59
Number of iterations

## Slide 23
Chart: System Unbalance (8 jobs ,4 machines)
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
Genetic | 411 | 18 | 18 | 10 | 6 | 10 | 18 | 25 | 6 | 18
Particle swarm | 576 | 65 | 18 | 18 | 7 | 18 | 10 | 6 | 7 | 6
Combined(NSGA & PSO) | 6 | 7 | 6 | 7 | 18 | 6 | 7 | 6 | 6 | 7
Number of iterations

## Slide 24
Chart: Throughput(8 jobs ,4 machines)
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
Genetic algorithm | 35 | 46 | 46 | 37 | 43 | 37 | 46 | 34 | 43 | 46
Particle swarm | 32 | 46 | 46 | 46 | 46 | 46 | 37 | 43 | 37 | 43
NSGA & NSPSO | 43 | 50 | 46 | 50 | 46 | 46 | 50 | 46 | 43 | 50
Number of iterations

## Slide 25
Chart: Penalty Cost(8 jobs ,4 machines)
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
Genetic algorithm | 111 | 93 | 72 | 93 | 93 | 74 | 72 | 72 | 74 | 72
Particle swarm | 101 | 93 | 72 | 72 | 59 | 72 | 74 | 70 | 72 | 70
NSGA & PSO | 93 | 59 | 59 | 59 | 72 | 72 | 59 | 70 | 70 | 59
Number of iterations

## Slide 26: Key Insights from the results
From the analysis we understand the effective data handling capability of NSGA and NSPSO algorithm. It is giving near optimal solution at population size of 20 and total generations of 50
From the graphs (Figure 1,2 and 3) in each algorithm as the number of iterations increases System unbalance and Penalty cost is minimized while throughput is maximized
From the graphs (Figure 4,5 and 6) NSGA & PSO algorithm gives more effective results. System unbalance has been reduced, throughput has been maximized and Penalty cost has been minimized.
The graphs are not always consistent in reducing a objective because we are considering Non dominated procedure for evaluation of Fitness which may result in elevation in graph although iterations increases

## Slide 27: Practical Implications/ Utility of Results
We have 8 jobs with 8! Job sequences. For one order it exist (9). (6). (6). (2). (2). (2). (1). (1). (1) = 2592 machine allocations for operations. With this we have 8! Type job sequences, so combining these two gives 8! . 2592= 10^9 combinations. Hence forth exhaustive search method will be practically not applicable
Practically in FMS traditional methods are being followed in job sequencing using predetermined sequencing rules(LIFO,FIFO,SPT,CR).But it may not always guarantee in optimal solutions. But from the above analysis we can conclude that we can achieve near optimal solutions in Multi objective environment reducing the stress and helping the job operator to avoid tedious calculations.

## Slide 28: Conclusion & Scope for Future Work
Here in this project we have tried to deal with multi objective problems in Manufacturing industry where large number of part types are processed on various machines. We provided a new meta-heuristic approach to handle this computational complexity involved in this project.
1. Developing a methodology for multi-objective optimization
2. Development of new solution representation scheme in linking both NSGA and PSO
3. We have introduced more complexity in this problem by consider three objectives which
differ in nature(Maximization and minimization.
Future research can be done along by including more complexity in this problem.
(Introducing travel time between the machines, increasing part types also increasing the number of objectives).
More realistic variables and constraints, such as the availability of pallets, jigs, fixtures, automatic guided vehicles (AGVs)
Consideration of multiple objective based on pareto dominance to balance conflicting constraints may give new direction in field of Meta heuristics as well as FMS

## Slide 29: Key References
Berrada and Stecke, 1986 M. Berrada, K.E. Stecke, A branch and bound approach for machine load balancing in flexible manufacturing systems,Management Science, 16 (10) (1986), pp. 1316–1335
D. Powell, M. Skolnick,Using genetic algorithm in engineering design optimization with non linear constraints,S. Forrest (Ed.), Proceedings of the ICGA-93, Morgan Kaufman, San Mateo, CA (1993), pp. 967–972
M.K. Tiwari, B. Hazarika, P. Jaggi, N.K. Vidyarthi, S.K. Mukhopadhya,A heuristic solution approach to the machine loading problem of an FMS and its petri net model, International Journal of Production Research, 35 (8) (1997), pp. 2269–2284
M.K. Tiwari, N.K. Vidyarthi, Solving machine loading problems in a flexible manufacturing system using a genetic algorithm based heuristic approach, International Journal of Production Research, 38 (4) (2000), pp. 3357–3384
S. Saravana Sankar ,S. G. Ponnanbalam,C. Rajendran,A multiobjective genetic algorithm for scheduling a flexible manufacturing system,International Journal of Advanced Manufacturing Technology (2003) 22: 229–236
Sandhyarani Biswas & S. S. Mahapatra, Modified particle swarm optimization for solving machine-loading problems in flexible manufacturing systems, International Journal of Advanced Manufacturing Technology (2008) 39:931–942